Revised Javelin Tip Design

for Ballista Missiles (2008)

* Hrelgar –

-- Shire of Nordenhal – East Kingdom – original redesign

* Master Jean Paul Pierrepont, OL

-- Great Household of the Dark Horde (GDH) -- Middle Kingdom ---

(Permission is given to copy as long as credit is given to the authors.)

Hrelgar wrote up the original changes, I rewrote them.  As long as the missiles meet the standards put forth by the society, you can use other materials ..

This design below has been tested.

OK,  as I (Jean Paul Pierrepont) or (known as JP) start this,

I will explain some of MY standard parts and quantities:

-----------------------------------------------------------------------------------------------------------

ONE -- SOLID Pool Noodle Blank--roughly  5.5 to 5.75 inches long

(I sell mine in sections approximately 28 1/2ish inch sections that are "UPS'able Each section can be cut into 5 pieces )

Don't EVEN think of using those that have the hole thru them! No No

ONE—2 ½ inch OD x 1/8 inch thick leather washer disks

The special disk to add the support for the shafting

ONE-- 1-5/16 / 1-3/8 inch – 1/8” thick leather washer disk

(The rules say, yellow poly pipe is normally 1 5/16th in diameter.)

(You can use 1-5/16th disks BUT the larger diameter is for safety if you want it)

ONE-- half of a cutup tennis ball (optional)

It makes a nice "THUMP" as it hits without hurting (adds 1 oz of weight)

When you see the tape.. All of it is 2 inch wide .  NOT the 1 3/4 inch width tape, it does make a difference in the way the taping, layers, and weight goes.  NOTE: 1 foot of tape adds .1 lb    Watch how much you use, it adds up quickly!

# Text boxes

Take a section of Pool Noodle (or closed cell foam) and cut it into 5 equal pieces. A full “Pool Noodle” you will get 10 pieces and each "noodle" will vary in length.

So measuring is a GOOD thing.

Noodle color may vary and does not mean a thing.

One piece will look like this

(5.5 to 5.75 inches long)

Cut a piece 1 ¾ to 2 inches wide for the collar.

Leaving a piece over 3 ½ inches long for the nose.

Cut an 1 ¼ inch hole thru the center

(NOTE:  I do mean center!)

of the collar section for a snug fit over the shaft and near the leather washer.

Sand a bevel from ¼ inch from the 1 ¼ hole thru to ½ to ¾ inch

up the side of the collar to help allow the tip to have a good fit and aerodynamics

(well as good as a plastic pipe with foam can get.)

Hmmmm

Somewhere along here I might tell you if you cut 3 inches off your ballista shafts,

you may save .8 of a pound

(that is if you are using 160 psi.)

On the top of the ballista shaft, you SHOULD put 2 pieces of strapping tape over the top of the tube and seal it up from water. That will help keep water from getting to the leather disk and destroying it.

THEN place (1) 5/16 to 1-3/8th inch diameter by 1/8" thick minimum HARD leather disk over the sealed shaft, then crossing 2 pieces of strapping tape, then wrapping  another piece around the tape on the shaft.

This will keep water getting to the leather disk and make sure it does not move, or get wet, moldy and destroyed.

Please Note: Fins are OPTIONAL as of this date. (4/1/2008) but the following Society rule applies.

“Javelins (bolts) must be stable in flight or have fletching made from flexible material to make them stable in flight.” If they fly really out of control, you really may need fins!!

They are a good thing.

Ok – Slide the beveled collar up the ballista shaft and make sure it is flush with the leather disk.

Ok – Put the 2 ½ X 1/8 inch leather disk on top of the collar assembly

and secure it by (2) crossed strips of strapping tape.

Then take a (2) short strips and wind it up from just below the collar

on the shaft toward the 2 ½ leather disk squeezing it down slightly to secure the collar to the shaft.

I put the tip on top of the collar assembly and use 6 short strips to secure it overlapping by ½ inch. Then do the strips over the top of the tip to the bottom of the collar and about 2”more making sure it’s snug.

And a small strip (not shown) over the bottom of the tape and up the collar securing it.

There are 3 wraps of strapping tape that start about an inch below the junctions of the two sections and overlap each other about ¾ inches toward the tip to keep it from bulging at impact.

Option Time – You do not HAVE to have a ½ tennis ball tip. You can just use rounded foam and save about 1 oz. BUT, I like the “thump factor”, plus it saves your tips. Make sure you hold your length.

From the bottom to the top of the foam, you have to have 3 inches minimum.

I use 4 inches so it still be there over time.

Add 1 to 2 small strips of yellow "duct tape" starting from the bottom of the tape and go up to to the bottom of the foam locking the first layer of duct tape onto the shaft.

I add (1) strip around the middle to help the strapping tape keep it all from bulging out.

I may not need it, but will see over time..

Now add strips over the top of the noodle tip with yellow "duct tape", making sure you overlap on the top and sides.

Make sure they DO NOT weigh more than 16 oz or they will FAIL!!!

Weigh & check them BEFORE you go to an event,

so you don’t look foolish!

Check them each time you pull them out!!

Make sure all of your bolts are identified in readable English with your name,  group, and kingdom.

See you on the field!   “JP”